## Slide 1
CHAPTER 10 / ENVIRONMENTAL SCIENCE
Renewable
Energy
What will power the light next?
SCIENCE → ISSUES → SOLUTIONS
01 / 48

## Slide 2
CHAPTER 10 / CENTRAL QUESTION
The Central question
02 / 48
Can we develop renewable energy resources to help sustain a thriving economy without adversely affecting the environment?
SCIENCE → ISSUES → SOLUTIONS → TAKEAWAYS

## Slide 3
CHAPTER 10 / SCIENCE
Samsø: an energy system, not a single device
03 / 48
Wind supplies electricity
Biomass and solar energy supply heat
Grid connections balance imports and exports
Offshore-wind photograph from the chapter opening.

## Slide 4
CHAPTER 10 / SCIENCE
Where renewable energy comes from
04 / 48
Primary source | Renewable pathways | Energy we use
Sunlight | Solar, wind, river flow, waves, biomass | Electricity, heat, fuels
Earth’s internal heat | Geothermal systems | Heat and electricity
Gravitational interactions | Ocean tides | Motion and electricity
Most pathways begin with sunlight. Geothermal energy and tides have different primary sources.

## Slide 5
CHAPTER 10 / SCIENCE
Three ways to use sunlight
05 / 48
Direct heating and daylight
Concentrating solar power makes heat
Photovoltaic cells produce electricity directly
Fig. 10.5: the Oberlin atrium uses sunlight for heat and daylight.

## Slide 6
CHAPTER 10 / SCIENCE
How a photovoltaic cell produces electricity
06 / 48
1 Light supplies energy
2 The junction separates charges
3 The external circuit powers a load
Adapted from Fig. 10.7: absorbed light creates mobile charges, and the junction separates them to drive an external circuit.

## Slide 7
CHAPTER 10 / SCIENCE
Experiment: does panel angle matter?
07 / 48
Relative direct-beam power (%)
Chart: 
| 0° | 30° | 60°
Relative direct-beam power (%) | 100 | 86.6025 | 50
Predict first
The same panel turns away from a fixed beam.
Which angle captures the least power?
At 60°, the panel intercepts half the direct-beam power.
Ideal direct-beam model, not measured PV performance. Angle is measured from the panel’s perpendicular direction.
Angle of the bean on the panel
% of Direct Beam Power

## Slide 8
CHAPTER 10 / SCIENCE
Concentrating solar power uses a heat engine
08 / 48
1 Mirrors concentrate sunlight
2 Heat transfers to a steam cycle
3 A turbine drives the generator
Adapted from Fig. 10.6 and §10.8: mirrors supply heat, while a separate steam cycle drives a generator.

## Slide 9
CHAPTER 10 / SCIENCE
A wind turbine converts motion to electricity
09 / 48
1 Aerodynamic forces turn the rotor
2 The shaft transfers mechanical energy
3 The generator produces electricity
Adapted from Fig. 10.8: moving air turns a rotor coupled to an electrical generator.

## Slide 10
CHAPTER 10 / SCIENCE
Magnus Effect
10 / 48
SPIN CHANGES THE FLOW. THE FLOW EXERTS A SIDEWAYS FORCE.
REAL SMOKE-TUNNEL EXPERIMENT
Watch the smoke
Air enters from the right.
When the cylinder spins,
the wake bends upward.
Air up. Force down.
The sideways force is
the Magnus effect.
Animation: MatSouffNC858s · Wikimedia Commons · CC BY-SA 4.0

## Slide 11
CHAPTER 10 / SCIENCE
Sea breezes reverse as land heats and cools
11 / 48
DAY • Near-surface air moves from sea to land.
NIGHT • Near-surface flow can reverse toward the sea.
Adapted from Fig. 10.9: different heating and cooling rates produce daily changes in coastal air circulation.

## Slide 12
CHAPTER 10 / SCIENCE
Hydropower uses a height difference
12 / 48
1 Water enters the penstock
2 Flow turns the turbine
3 Water returns to the downstream river
Adapted from Fig. 10.12: water loses gravitational potential energy as it passes through a turbine.

## Slide 13
CHAPTER 10 / SCIENCE
Experiment: doubling the water drop
13 / 48
Calculated electrical power (kW)
Chart: 
| 10 m head | 20 m head
Calculated electrical power (kW) | 78.48 | 156.96
Hold flow constant
What happens to power when the height difference doubles?
Twice the head gives twice the power, if flow and efficiency stay constant.
Calculated classroom example: flow = 1 m³/s, efficiency = 80%, water density = 1,000 kg/m³.

## Slide 14
CHAPTER 10 / SCIENCE
Tides and waves have different energy sources
14 / 48
Low tide
High tide
Tides follow gravitational cycles. Most surface waves gain energy from wind.
Fig. 10.14: low and high tide at Hopewell Rocks, Bay of Fundy.

## Slide 15
CHAPTER 10 / SCIENCE
Geothermal energy transfers Earth’s heat
15 / 48
1 Hot water brings heat to the surface
2 A second fluid vaporizes and drives a turbine
3 Cooled geothermal water returns underground
Adapted from Fig. 10.19: a binary-cycle plant transfers geothermal heat to a separate working fluid.

## Slide 16
CHAPTER 10 / SCIENCE
Biomass stores energy in chemical bonds
16 / 48
Wood and other biomass can burn directly
Sugars and starches can become ethanol
Oils and fats can become biodiesel
Fig. 10.35, excerpt: harvested corn is one possible biofuel feedstock.

## Slide 17
CHAPTER 10 / SCIENCE
Cellulosic ethanol requires an extra breakdown step
17 / 48
1 Cellulose contains linked sugar units
2 Enzymes make sugars accessible
3 Microbes ferment the sugars
Adapted from Fig. 10.23: pretreatment and enzymes release sugars before fermentation and ethanol recovery.

## Slide 18
CHAPTER 10 / SCIENCE
Quick quiz: which examples use a turbine?
18 / 48
01
Photovoltaic solar electricity
No. A semiconductor converts light directly.
02
Concentrating solar electricity
Yes. In our example, a steam turbine drives a generator.
03
Hydroelectric power
Yes. Moving water turns the turbine.
Discuss each pathway before revealing its answer.

## Slide 19
CHAPTER 10 / SCIENCE
Science summary
19 / 48
10.1
Solar energy can provide heat or generate electricity.
Photovoltaics and concentrating solar use different mechanisms.
10.2
Wind and water supply mechanical energy.
Geothermal systems use Earth’s internal heat.
10.3
Biomass stores chemical energy.
Fuel production requires processing and energy input.

## Slide 20
CHAPTER 10 / ISSUES
Main environmental and social issues
20 / 48
Habitat loss, fragmentation, and new transmission corridors
Water demand and competition with other uses
Bird and bat mortality near turbines and power lines
Changed river flows, sediments, water quality, and fish migration
Displacement of communities and loss of livelihoods
Competition for agricultural land, food, and water
Impacts depend on the technology, location, scale, and operating practices.

## Slide 21
CHAPTER 10 / ISSUES
A sunny landscape is also a habitat
21 / 48
Land clearing removes habitat
Roads and fences interrupt movement
Construction can damage burrows and drainage
Fig. 10.25: roads can fragment desert bighorn sheep habitat.

## Slide 22
CHAPTER 10 / ISSUES
Concentrating solar power can compete for water
22 / 48
Steam-cycle cooling can consume water
Strong solar resources often occur in dry regions
Cooling design changes the water requirement
Fig. 10.6a: a tower-based solar plant. Cooling requirements differ from those of photovoltaic panels.

## Slide 23
CHAPTER 10 / ISSUES
Energy return on energy investment
23 / 48
Useful energy obtained
200 units
Energy invested
40 units
EROEI = energy out ÷ energy in
200 ÷ 40 = 5 | Net energy = 160 units
Illustrative calculation, not a measured value for a particular fuel or technology.

## Slide 24
CHAPTER 10 / ISSUES
Wind development affects birds and bats
24 / 48
Bird collisions
Bat fatalities
Risk depends on species, location, migration, and turbine operation.
Figs. 10.28 and 10.30: a golden eagle and eastern red bats illustrate vulnerable wildlife.

## Slide 25
CHAPTER 10 / ISSUES
Transmission corridors extend the footprint
25 / 48
Birds may collide with power lines
New roads and corridors can divide habitats
Some grassland birds avoid tall structures
Risk extends beyond the turbine or solar-panel boundary
A project assessment must include the connections that deliver its electricity.

## Slide 26
CHAPTER 10 / ISSUES
A dam changes an entire river system
26 / 48
Reservoirs trap sediments
Dams interrupt fish migration
Water temperature and oxygen can change
Flooded organic matter can produce greenhouse gases
Fig. 10.13: the Three Gorges project illustrates the scale of large hydroelectric development.

## Slide 27
CHAPTER 10 / ISSUES
Hydropower benefits and costs reach different people
27 / 48
Electricity may serve distant cities
Flooding can displace households
Fishing, farming, and cultural sites can be lost
Affected communities need a meaningful voice
Fig. 10.34: a resident in a partly demolished home before inundation by the Three Gorges reservoir.

## Slide 28
CHAPTER 10 / ISSUES
Biofuel demand can change food and land systems
28 / 48
Diverse prairie
Intensive crop production
Food competition, fertilizer runoff, soil loss, and habitat conversion can occur along the fuel pathway.
Fig. 10.36: contrasting ecosystems illustrate the consequences of converting land to intensive agriculture.

## Slide 29
CHAPTER 10 / ISSUES
Comparing complete renewable-energy pathways
29 / 48
Pathway | Main pressures | Questions before development
Solar | Land, materials, cooling water for thermal systems | Which site and cooling design?
Wind | Wildlife, roads, transmission corridors | Which species, seasons, and routes?
Hydropower | River change, flooded land, displacement | What happens upstream and downstream?
Biofuels | Food and land competition, runoff, soil loss | Which feedstock and production boundary?
A chapter synthesis. Local conditions determine the importance of each pressure.

## Slide 30
CHAPTER 10 / ISSUES
Issues summary
30 / 48
10.4
Solar development can affect habitats and water supplies.
10.5
Wind turbines and transmission lines can harm wildlife.
10.6
Dams alter rivers and can displace communities.
10.7
Biofuel expansion can compete with food and damage ecosystems.

## Slide 31
CHAPTER 10 / SOLUTIONS
Solar siting can reduce habitat damage
31 / 48
Use suitable rooftops and developed sites
Check structural, shading, and grid constraints
Reduce pressure on intact habitats
Fig. 10.40: rooftop photovoltaic systems in Freiburg, Germany.

## Slide 32
CHAPTER 10 / SOLUTIONS
Storage shifts energy in time
32 / 48
Storage approach | What is stored? | What must be checked?
Thermal storage | Heat, for example in molten salt | Heat loss and usable temperature
Batteries | Electrochemical energy | Power, usable capacity, and losses
Pumped storage | Water at higher elevation | Reservoirs, water, and terrain
Stored energy can serve later demand, but every storage system has limits and losses.

## Slide 33
CHAPTER 10 / SOLUTIONS
Storage challenge: is the evening covered?
33 / 48
Energy (MWh)
Chart: 
| Charged | Delivered | Demand
Energy (MWh) | 2 | 1.6 | 2
Efficiency = 80%
2.0 MWh goes in.
Can storage supply the whole evening?
1.6 MWh delivered. Another 0.4 MWh must come from elsewhere.
Classroom assumptions: 2.0 MWh charged, 80% round-trip efficiency, 2.0 MWh evening demand.

## Slide 34
CHAPTER 10 / SOLUTIONS
Wind design and siting can reduce harm
34 / 48
Older lattice towers
Newer tubular towers
Repowering can reduce some bird risks. Careful siting and monitoring remain essential.
Fig. 10.42: turbine designs differ in perch availability and operating characteristics.

## Slide 35
CHAPTER 10 / SOLUTIONS
Experiment: changing turbine operation protects bats
35 / 48
Reduction in bat fatalities (%)
Chart: 
| Higher wind trigger | Blade-angle change
Reduction in bat fatalities (%) | 60 | 57.5
Tested on 21 turbines
Reduce rotor motion during low-wind periods when bats are at risk.
Fewer fatalities—not zero risk. Site-specific evidence matters.
Baerwald et al. (2009): reductions relative to normal operation at one Alberta site during the peak fatality period.

## Slide 36
CHAPTER 10 / SOLUTIONS
Safer transmission routes and visible lines
36 / 48
Avoid important flight, feeding, and roosting areas
Use suitable existing rights of way
Mark high-risk spans and measure the outcome
Fig. 10.44: markers make electrical lines more visible to birds.

## Slide 37
CHAPTER 10 / SOLUTIONS
Run-of-the-river hydropower preserves some flow
37 / 48
1 Divert only part of the river
2 Maintain ecological flow
3 Provide fish passage and monitor impacts
Adapted from Figs. 10.45–10.46: a diversion supplies a powerhouse while the main channel retains flow and fish passage.

## Slide 38
CHAPTER 10 / SOLUTIONS
Existing dams can offer alternatives to new barriers
38 / 48
Assess suitable existing unpowered dams
Improve fish passage and operating rules
Compare refurbishment with removal and other options
Fig. 10.46: a fish bypass at a low dam illustrates one approach to maintaining passage.

## Slide 39
CHAPTER 10 / SOLUTIONS
Lower-impact biofuels start with the feedstock
39 / 48
Use appropriate residues and waste streams
Protect forests, soils, and food production
Evaluate algae and cellulosic pathways over their full life cycle
Fig. 10.50: algae cultivation is a potential biofuel pathway, with its own resource and processing requirements.

## Slide 40
CHAPTER 10 / SOLUTIONS
Policy and community participation shape deployment
40 / 48
Clear permitting and grid-connection processes
Financing and incentives aligned with environmental goals
Enforceable habitat and land-use protections
Meaningful community participation and fair distribution of benefits
Technical design and social decisions jointly determine the outcome.

## Slide 41
CHAPTER 10 / SOLUTIONS
Solutions summary
41 / 48
10.8
Solar: improve siting, cooling design, and storage.
10.9
Wind: reduce wildlife exposure through siting and operation.
10.10
Hydropower: maintain river function and assess existing barriers.
10.11
Biofuels: protect ecosystems and choose suitable feedstocks.

## Slide 42
CHAPTER 10 / APPLICATION
Grid challenge: four hours after sunset
42 / 48
DEMAND
10 MW
WIND
3 MW
HYDRO
4 MW
SOLAR (Photovoltaic)
0 MW
BATTERY
3 MW maximum • 12 MWh usable
Can the lights stay on for all four hours?
Gap = 3 MW × 4 hours = 12 MWh. Yes—exactly enough in this model.
Hypothetical isolated system. Battery starts full with 12 MWh usable output and a 3 MW discharge limit.

## Slide 43
CHAPTER 10 / APPLICATION
Grid challenge: the wind drops
43 / 48
DEMAND
10 MW
WIND
1 MW
HYDRO
4 MW
0 MW
BATTERY
3 MW maximum • 12 MWh usable
Is the battery enough now? Propose a response.
Gap: 5 MW for 4 hours = 20 MWh. Reduce demand by 2 MW, or add 2 MW of reliable supply.
Same four-hour scenario, but wind now supplies 1 MW throughout the period. No automatic grid imports are available.
SOLAR (Photovoltaic)

## Slide 44
CHAPTER 10 / TAKEAWAYS
What students should take away
44 / 48
Mechanism
Trace energy from its primary source to useful output.
Consequences
Include land, water, wildlife, and affected communities.
Design
Match the solution to the specific impact and location.
Reliability
Check both the rate of supply and how long it can last.

## Slide 45
CHAPTER 10 / CENTRAL QUESTION
Returning to the central question
45 / 48
Can we develop renewable energy resources to help sustain a thriving economy without adversely affecting the environment?
Renewables can support a thriving economy while reducing many harms. Their environmental performance depends on where and how we build and operate the system.
Zero impact is not a realistic promise
Lower demand, careful siting, and verified safeguards improve the outcome

## Slide 46
CHAPTER 10 / TAKEAWAYS
Renewable energy and you
46 / 48
Reduce avoidable energy use
Choose efficient buildings, appliances, and transport where feasible
Evaluate energy proposals using evidence
Participate in local decisions and ask who benefits
Individual choices matter alongside action by institutions, industry, and government.

## Slide 47
CHAPTER 10 / DISCUSSION
Exit questions
47 / 48
01
Why can a renewable energy project still harm an ecosystem?
Infrastructure, resource use, and operation can change habitats and communities.
02
Which change could reduce bat fatalities at a wind farm?
Reduce rotor motion during high-risk low-wind periods, then monitor results.
03
Why is a 3 MW battery rating insufficient to describe its usefulness?
We also need usable MWh capacity to know how long it can supply power.
Explain a mechanism, a mitigation, and one limitation.

## Slide 48
CHAPTER 10 / REFERENCES
Sources and further reading
48 / 48
PRIMARY COURSE SOURCE
Molles & Borrell (2016)
Environment: Science, Issues, Solutions
Chapter 10 · Renewable Energy
MECHANISMS AND EMPIRICAL EVIDENCE
U.S. Department of Energy · solar, wind, geothermal, and storage
Baerwald et al. (2009) · turbine operation and bat fatalities
The Journal of Wildlife Management · doi:10.2193/2008-233
Practice Chapters 9 and 10 in the Exam Center
emohellebi.github.io/teaching/courses/environmental-science/exam-center/